## Slide 1
Intensity Interferometry at Calern and beyond: towards wavelength multiplexing and the resolution of Sirius B
William Guerin for the I2C consortium (Intensity Interferometry at Calern)
Institut de Physique de Nice (INPHYNI)
Université Côte d’Azur & CNRS
https://inphyni.univ-cotedazur.eu/sites/cold-atoms
Notes: Bleus UCA (RVB):
Bleu clair: 0, 175, 215  titres de slides et bandeau de pied de page
Bleu moyen: 0, 150, 188
Bleu foncé: 0, 126, 161  Nom/affiliation du slide titre, réferences, flèches.
Couleurs flashy de la charte graphique UCA:
Magenta: 229, 0, 91
Orange: 249, 176, 0
Vert: 149, 193, 31

## Slide 2
The I2C consortium
Former members: Antoine Dussaux
(Post-doc, 2015-2016)
Antonin Siciak
(PhD student, 2018-2021)
Nolan Matthews
(Post-doc, 2021-2023)
Géoazur, MéO team (OCA)
Julien Chabé
Clément Courde
INPHYNI, cold-atom team
William Guerin
Robin Kaiser
Guillaume Labeyrie
Mathilde Hugbart
Tolila Sarah
Ilian
Ellafi
Federico
Izraelevitch
Andreas
Zmija
Lagrange (OCA)
Jean-Pierre Rivet
Olivier Lai

## Slide 3
Calern
Telescopes, altitude = 1280 m
30 km

## Slide 4
Our approach: SII with optical telescopes
C2PU, Ø = 1 m, B = 15 m
SOAR, Ø = 4.1 m
Drawback: - Large arrays of large optical telescopes will never be available
Advantages:
Methodology:
Step-by-step progress
Tests and calibrations in the lab
On-sky demonstrations at Calern
Go to bigger facilities…
C2PU, Ø = 1 m, B = 15 m
MéO, Ø = 1.5 m
T1M, Ø = 1 m
ATs, Ø = 1.7 m
The small PSF allows using the best detectors and other photonic technologies (fibers, narrow filters, etc.)
The instrument can be adapted to any existing facility
No issue with the sky background

## Slide 5
Outline
First generation instrument (2015-2024):
Second generation instrument (work in progress):
Brief summary of what we did so far
Wavelength multiplexing in the blue
Towards the resolution of Sirius B

## Slide 6
Brief summary of what we’ve done so far
Rivet et al., MNRAS 494, 218 (2020)
Dussaux et al., PRA 93, 043826 (2016)
2015
2016
2017
2018
2019
2020
Learning how to measure sub-nanosecond intensity correlation, test on light scattered by a hot vapor
Feasibility study + design + lab test of a telescope instrument
Feb.: Bunching with star light (one telescope)
Oct.: Intensity interferometry with two telescopes
Aug.: SII at Ha on P Cygni, refinement of the star’s distance
Apr.: Bunching at SOAR in one night (h Car)
Feb.: SII at Ha on Rigel
Aug.: SII at Ha on P Cygni (again)
Proposal for SII with segmented mirrors (I3T concept)
Gori et al., MNRAS 505, 2328 (2021)
Guerin et al., MNRAS 472, 4126 (2017);
MNRAS 480, 245 (2018)
de Almeida et al., MNRAS 115, 1 (2022)
Guerin et al., Proc. SF2A 2021, p. 331

## Slide 7
Brief summary of what we’ve done so far
2021
2022
ANR project starts (€€)
Jan.: SII on g Cas between the laser ranging telescope and a 1 m mobile telescope
March: Technical run (6 nights) at Paranal on two ATs at their maintenance station (separation 49 m)
Matthews et al., Proc. SPIE 12183, 121830 (2022)
Matthews et al., Astron. J. 167, 117 (2023)
2023
May: Technical run (5 nights) at Paranal on three ATs at standard stations
2024
2025
June: First lab test of multiplexing Nch = 5
ERC project starts (€€€€€)
Tolila et al., Proc. SF2A 2024, p. 197
Extension of I3T
Matthews et al., MNRAS 538, 867 (2025)
Adding tip-tilt correction…

## Slide 8
First generation instrument
Filter width Dl = 1 nm (tc ~ 1 ps)
l = 780 nm or 656 nm (Ha)
Light injected in MMF (Ø = 100 µm)
Detectors tel ~ 500 ps (FWHM)
Time tagger from Swabian Instrument
Photon-counting regime (shot-noise limited)
Compact and transportable
Real-time computation of the g(2)
Two polarization channels
Tip-tilt correction
Main features:
Technical details:
How to transport a stellar interferometer:

## Slide 9
What we want (as everyone):
Better detectors: lower timing jitter & good quantum efficiency
Wavelength multiplexing
Adaptable to large telescopes and long baselines
Excellent throughput
Towards a second-generation instrument
Dalal et al., Phys. Rev. D 109, 123029 (2024)
Guerin et al., Comptes Rendus. Phys., in press (2025); arXiv:2503.22446
To do what ? The design depends on the objectives…

## Slide 10
Goal: partial resolution of Sirius B
Sirius B: the closest and brightest white dwarf (“mind-blowing“ in Saha’s plot), mB = 8.4
No angular diameter of a white dwarf has even been measured directly (evaluated from photometry)
Why ? Needs baseline ~ 1 km !
Right time to do it (separation ~ 11”) !
Notes: Separation challenging (impossible) for a Cherenkov telescope

## Slide 11
Where to do it ?
Larger baselines:
Subaru – Gemini: 790 m
Keck I – Gemini: 630 m
Keck I – CFHT: 630 m
800 m
(Another possibility could be at Paranal: UTs – Vista : ~1.5 km, but more complicated access…)
Olivier Lai is well introduced there…

## Slide 12
At which wavelength ?
Even 800 m is not enough: the shorter the better !
l = 420 nm
Notes: Radius of Sirius B from: spectrum + photometry + parallax
Sirius B: A New, More Accurate View
J. B. Holberg, M. A. Barstow, F. C. Bruhweiler, A. M. Cruise, and A. J. Penny
Spectrum of Sirius B: data from HST:
Hubble Space Telescope Spectroscopy of the Balmer lines in Sirius B†
M.A. Barstow, Howard E. Bond, J.B. Holberg, M.R. Burleigh, I. Hubeny and D. Koester

## Slide 13
With which detectors ?
Inspired by the Erlangen group (J. von Zanthier): LINPinx from Photonscore
QE ~ 33% @ 420 nm
Jitter ~ 30 – 35 ps (FWHM)
Negligible dark count, low dead time (max count rate ~ 100 MHz)
Diameter = 8 mm !!!
Leopold et al., JATIS 11, 035005 (2025)
 Tested on sky (Sept. 2025)

## Slide 14
Wavelength multiplexing
Big detectors…  Easy to focus light onto it without losses
 Not scalable to many channels
Buy 32 detectors !
16 channels × 2 telescopes

## Slide 15
How to disperse the light ?
Preliminary design based on 3 optical elements:
See Ilian Ellafi’s poster
Diffraction grating
Echelon to compensate the grating’s temporal dispersion
Slicer to increase the spatially separation between the wavelengths
Katz et al., Rev. Sci. Instrum. 87, 11E535 (2016)

## Slide 16
Integration to the telescopes
Compact coupling module
Adapted to each telescope,
has to reject Sirius A
GRIN MMF Ø = 400 µm
(Exail photonics)
NA = 0.12
Dispersion < 1 ps/m
Transmission > 80% for 10 m
Multichannel instruments
Same for all telescopes, doesn’t move,
can be well calibrated in the lab
Strategic plan :
1- First test on one Keck
2- Duplicate + interferometry (baseline = 85 m)
3- Adapt to CFHT + long-baseline interferometry (630 m)
4- Convince Gemini and adapt ( larger area)
5- Convince Subaru and adapt ( longer baseline: 790 m)
Bent Cassegrain @ Keck

## Slide 17
Feasibility assessment
a ≈ 0.33 (QE) × 0.8 (atm.) × 0.8 (fiber) × 0.8 (grating) × 0.8 (other) ≈ 0.13
Nph(λ = 420 nm) = 4.6 × 10-8 photons/m2/s/Hz (from HST calibrated spectrum)
with Ai = 76 m2 (Keck), 8.4 m2 (CFHT), 48.4 m2 (Gemini), 51.3 m2 (Subaru)
|V2| ≈ 0.9
tel ≈ 25 ps rms (2 detectors + TDC + others)
Nch = 16
SNR = 10 reached in …
Tobs = 46 h for Keck – CFHT (630 m)
Tobs = 8 h for Keck – Gemini (630 m)
Tobs = 12 h for Subaru – Gemini (790 m)
For a precise determination of the angular diameter: needs larger baselines !
UTs – Vista (1.5 km) @ Paranal or GTC – WHT (1.1 km) @ Roque de Los Muchachos
Notes: Expected count rate around 330 kcps/channel with these numbers
Effect not included: reduction of the SNR due to non-square spectra

## Slide 18
18
Thank you !
(Picture by Serge Brunier)
https://inphyni.univ-cotedazur.eu/sites/cold-atoms/research/i2c
Guerin et al., MNRAS 472, 4126 (2017)
Guerin et al., MNRAS 480, 245 (2018)
Rivet et al., Exp. Astron. 46, 531 (2018)
Lai et al., Proc. SPIE 10701, 1070121 (2018)
Rivet et al., MNRAS 494, 218 (2020)
Gori et al., MNRAS 505, 2328 (2021)
Guerin et al., Proc SF2A (2021)
de Almeida et al., MNRAS 515, 1 (2022)
Matthews et al., Proc. SPIE 12183, 121830G (2022)
Matthews et al., Astron. J. 167, 117 (2023)
Tolila et al., Proc. SF2A, p. 197 (2024)
Matthews et al., MNRAS 538, 867 (2025)
Guerin et al., Comptes Rendus. Physique, in press (2025)

## Slide 19
Why not use SPAD arrays ?
Conservation of étendue (or “optical extent”): A W = cst
Seeing = 0.65” = 3.2 µrad (median seeing on Maunea Kea)
A = (8 m)2
with AO: low throughput  (and in the blue anyway…)
without AO: VERY hard to focus on small-area detectors
Big telescopes, either:
If you want to focus on, say, A’ = (20 µm)2, you need NA = 0.98 !!!
If you focus with a large NA, say NA = 0.5 (i.e. 30°) (without aberration!), you’ll get A’ = (50 µm)2.
That’s also why we want to use MMF with Ø = 400 µm (NA = 0.12)…

## Slide 20
SPAD arrays with small telescopes
SPADl from PIimaging
Linear array of 320 pixels
Pixel size = 18 µm, pitch = 28 µm, 80% fill factor with microlenses (limited NA)
Jitter 90 ps (FWHM), QE = 50% @ 500 nm
Expected SNR using the ATs at Paranal: (free one week /month !!!)
 mag. 6 in one night, 7 in one week
Notes: Parameters:
tau_et = 50 ps
QE = 80%
In the red
Visibility = 0.5
Obstruction and all losses taken into account (bona fide)

## Slide 21
Limitations to the SNR
Not useful to improve the detectors’ jitter tel beyond the coherence time tc.
For a given spectral range, increasing the number of channels increases tc  the SNR saturates.
Example:
tel = 10 ps
Dl = 0.1 nm @ 500 nm
tc = 8 ps < tel OK
Then if Nch = 2000
 Dltot = 200 nm !
Guerin et al., Comptes Rendus. Phys., in press (2025); arXiv:2503.22446

## Slide 22
Sirius B
Chandrasekhar, MNRAS 95, 207 (1935)
Bond et al., ApJ 840, 70 (2017)

## Slide 23
First lab tests of wavelength multiplexing
Single SNRs between 21 and 32  S(SNR2) = 59
Measured SNR on the total curve: 51. Not bad, but averaging not optimum!
Tolila et al., Proc. SF2A, p. 197 (2024)

## Slide 24
Noise
Matthews et al., Proc. SPIE 12183, 121830 (2022)
Spurious correlations (induced by the TDC and/or by cross talk between APDs)
 avoided using cable (electronic or optical) delays.
Measurement limited by photon statistics down to 1% (at least).
Coherence time agrees with the measured spectral filter.

## Slide 25
Some astrophysical measurements: P Cygni’s distance
Spectroscopy
Stellar model (CMFGEN)
Physical size
(luminosity distribution)
Angular size
(luminosity distribution)
Distance
Visibility measurements
Rivet et al., MNRAS 494, 218 (2020)
Almeida et al., MNRAS 515, 1 (2022)